## Slide 1
Q1 Fit Diagnostics
Spray penetration curve-fit quality, translated for mechanical engineering review
Main message: the clean CDF fits are generally usable for synthetic data generation. Median RMSE is 1.25 mm and median R2 is 0.9969.
23,008
candidate CDF plume traces
20,998
clean accepted fits (91.3%)
1.25
median RMSE [mm]
2.56
95th percentile RMSE [mm]
90.0%
clean and RMSE < 3 mm
What is being checked:
- Does the simplified curve follow measured spray penetration closely enough?
- Do the fitted constants move in physically sensible directions with pressure and nozzle geometry?
- Are optimization failures or parameter ambiguity likely to contaminate the exported data?
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py

## Slide 2
From Video Measurements To Diagnostics
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
1. Raw plume series
Penetration in mm vs time for each plume
->
2. Clean and align
Remove early zeros, bad jumps, negative values, and align onset
->
3. Fit q1 curve
Least-squares fit of onset-ramped t^(1/4) penetration
4. Quality gates
Keep plausible fits, reject outliers and weak traces
->
5. Aggregate
Pool clean rows and per-frame residuals
->
6. Diagnose
RMSE, residuals, convergence, parameter uncertainty
Code map: prepare_cleaned_series -> fit_quarter_only -> apply_filter_masking -> fit_diagnostics.run_all

## Slide 3
The Fitted Curve In Plain Terms
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
S(t) = sigmoid((t - t0) / s) * k * t^(1/4)
The sigmoid is a smooth valve: before onset penetration is near zero, after onset the curve follows a quarter-root growth law.
k
growth scale. Median fitted k = 446 mm/s^(1/4)
t0
onset time. Median = 0.309 ms
s
transition width. Median = 0.146 ms
Mechanical interpretation:
- k says how aggressively the visible penetration grows after onset.
- t0 says when the plume becomes visible after hydraulic delay correction.
- s says how sharply the plume turns on. Very large or nonphysical values are rejected.

## Slide 4
Quality Gates Keep The Exported Curves Conservative
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
2,010
flagged CDF fits
91.3%
clean survival rate
0.76-1.80
middle 50% RMSE [mm]
517,529
clean per-frame points
Most rejected fits are statistical outliers:
- robust outlier: 2,000
- basic gate failed: 30
- 5 ms penetration out of range: 29
Hard plausibility checks include:
- solver success and finite RMSE
- at least 10 valid points
- 0 < t0 < measured time range
- s < 1 ms and t0 < 0.8 ms
- penetration at 5 ms between 18 and 300 mm
Engineering read: the deck focuses on clean rows; flagged rows are kept separately for audit, not mixed into training-quality data.

## Slide 5
Fit Error Across Operating Conditions
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
What to look for:
- Lower values mean the fitted curve is closer to the measured plume.
- Overall median RMSE is 1.25 mm; 95% are below 2.56 mm.
- Error is not uniform: the pressure condition matters.
Lowest median-RMSE cells:
- Pinj 1600 bar, Pch 35.00 bar: 0.62 mm
- Pinj 1400 bar, Pch 35.00 bar: 0.62 mm
- Pinj 2200 bar, Pch 35.00 bar: 0.97 mm
Highest median-RMSE cells:
- Pinj 2200 bar, Pch 5.00 bar: 1.80 mm
- Pinj 2200 bar, Pch 15.00 bar: 1.62 mm
- Pinj 1600 bar, Pch 5.00 bar: 1.51 mm

## Slide 6
Per-Nozzle Fit Error
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Nozzle comparison:
- Boxes summarize the spread of RMSE by nozzle.
- The fitted model performs best when the curve shape is repeatable within the nozzle and condition.
Median RMSE by nozzle:
- Nozzle7: 0.94 mm, p95 1.84 mm
- Nozzle3: 1.07 mm, p95 2.11 mm
- Nozzle4: 1.16 mm, p95 2.40 mm
- Nozzle5: 1.16 mm, p95 2.33 mm
- Nozzle2: 1.24 mm, p95 2.37 mm
- Nozzle0: 1.27 mm, p95 2.65 mm
- Nozzle1: 1.34 mm, p95 2.34 mm
- Nozzle6: 1.35 mm, p95 2.53 mm
- Nozzle8: 1.40 mm, p95 2.46 mm

## Slide 7
Do The Parameters Move Like Physics Suggests?
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Most important result:
- k scales as DeltaP^0.53, rho_air^-0.24, diameter^0.48.
- Signs match the expected trend: higher pressure drop and larger holes increase penetration; higher chamber density reduces it.
Caution:
- Simple pressure-density-diameter scaling explains only R2 = 0.33 for k.
- t0 and s have lower R2, so onset and transition width also depend on imaging, plume interaction, and cleaning details.

## Slide 8
Residuals Show Where The Curve Is Biased
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Residual = fitted penetration - measured penetration.
- At 0.05 ms: median residual 1.74 mm.
- Around 0.95 ms: median residual 0.07 mm.
- At 1.55 ms: median residual -1.64 mm, but only 170 points.
Engineering read:
- The curve is close to unbiased after the initial transient.
- Early time is the hardest region because onset timing and image thresholding dominate.
- Late-time bins have low sample count, so do not over-interpret the tail.

## Slide 9
The Solver Is Not The Bottleneck
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Termination summary:
- ftol_satisfied: 20,937 fits, median nfev 40
- ftol_and_xtol_satisfied: 60 fits, median nfev 42
- gtol_satisfied: 1 fits, median nfev 27
No max-iteration failure appears in the clean-row summary. Most fits stop because further improvement in cost becomes tiny.

## Slide 10
Parameter Identifiability
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
What this means:
- Typical log-space std: k 0.020, t0 0.032, s 0.069.
- These are small enough that the fitted curves are stable.
Important caveat:
- k, t0, and s are correlated, especially k with s.
- Use the full fitted curve for engineering comparison. Avoid over-interpreting a single parameter by itself.

## Slide 11
How To Use These Results
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Use clean fits for:
- generating synthetic penetration trajectories
- training downstream MLP models
- comparing conditions with a compact curve representation
- estimating time-dependent residual spread
Do not use them blindly for:
- diagnosing individual failed plumes without checking flagged plots
- claiming t0 or s are pure physical delays
- extrapolating after the measured time range
- treating late residual bins with low counts as final truth
Recommended next checks: inspect the highest-RMSE conditions, tighten early-onset alignment if needed, and report RMSE plus residual sigma(t) when using synthetic data.

## Slide 12
File And Code Map
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Primary fitting code:
- MLP/curve_fit/fit_raw_data.py
- Model: spray_penetration_model_quarter_only
- Fit: fit_quarter_only uses scipy least_squares with Huber loss
- Filtering: apply_filter_masking creates clean and flagged rows
- End of script: summarize_dataset, summarize_filter_survival, fit_diagnostics
Diagnostics used in this deck:
- MLP/synthetic_data/fit_diagnostics/error_by_condition
- MLP/synthetic_data/fit_diagnostics/param_distributions
- MLP/synthetic_data/fit_diagnostics/residual_structure
- MLP/synthetic_data/fit_diagnostics/convergence
- MLP/synthetic_data/fit_diagnostics/identifiability

## Slide 13
Bottom Line For Review
q1 fit diagnostics
Source: MLP/synthetic_data/fit_diagnostics and MLP/curve_fit/fit_raw_data.py
Accepted q1 fits are accurate enough for the intended surrogate-data role: median error 1.25 mm, p95 2.56 mm, and 91.3% of CDF candidates survive cleaning.
Decision points:
- Green light for using clean q1 CDF rows as compact synthetic data.
- Keep flagged rows out of training unless manually reviewed.
- If early-time accuracy matters most, improve onset alignment before changing the curve law.
- If individual parameter interpretation matters, add a parameter-correlation caveat to reports.